This table is taken from the Construction page of the COSS website:
http://www.dtascommunityownership.org.uk

| RIBA work stages and description of main activities |
| --- |
| Overall Stage | RIBA Work Stages | Main Activities | Main Client Input |
| Preparation | Work Stage A Appraisal | Identification of client's needs and objectives, business case and possible constraints on development. Preparation of feasibility studies and assessment of options to enable the client to decide whether to proceed | Approval of brief Option appraisal and outline business case Selection and agreement of consultant professionals and Procurement method(s) |
|  | Work Stage B Design Brief | Development of initial statement of requirements into the Design Brief by or on behalf of the client confirming key requirements and constraints. Identification of procurement method and procedures, organisational structure and range of consultants and others to be engaged for the project. |  |
| Design | Work Stage C Concept | Implementation of Design Brief and preparation of additional data. Preparation of Concept Design including outline proposals for structural and building services systems, outline specifications and preliminary cost plan. Review of procurement route. | Input to specification Approval of final designs |
|  | Work Stage D Design Development | Development of concept design to include structural and building services systems, Updated outline specifications and cost plan. Completion of Project Brief. Application for detailed planning permission. |  |
|  | Work Stage E Technical Design | Preparation of technical design(s) and specifications, sufficient to co-ordinate components and elements of the project and information for statutory standards and construction safety. |  |
| Pre-Construction | Work Stage F Production Information F1 F2 | Preparation of production information in sufficient detail to enable a tender or tenders to be obtained. Application for statutory approvals. Preparation of further information for construction required under the building contract | Tender Review and contractor selection Final Procurement and contract approvals |
|  | Work Stage G Tender Documentation | Preparation and/or collation of tender documentation in sufficient detail to enable a tender or tenders to be obtained for the project |  |
|  | Work Stage H Tender Action | Identification and evaluation of potential contractors and/or specialists for the project. Obtaining and appraising tenders; submission of recommendations to the client |  |
| Construction | Work Stage J Mobilisation | Letting the building contract, appointing the contractor. Issuing of information to the contractor. Arranging site hand over to the contractor | Receive progress reports Site visits Approval of amendments |
|  | Work Stage K Construction to Practical Completion | Administration of the building contract to Practical Completion. Provision to the contractor of further Information as and when reasonably required. Review of information provided by contractors and specialists |  |
|  | Work Stage L Post Practical Completion L1 L2 L3 | Administration of the building contract after Practical Completion and making final inspections. Assisting building user during initial occupation period. Review of project performance in use |  |